## Slide 1: iFBalance Robot
Shantanu Sen Gupta
Manager, Research Institute
www.koreaits.com
STEAM AI Education Platform
(주)인디프로그

## Slide 2
iFBalance
+
AI
Notes: delete

## Slide 3
iFBalance
Day1
Day 3
Day 4
Day 2
Notes: delete

## Slide 4
Features
iFBalance

## Slide 5
iFBalance

## Slide 6
iFZero Module
iFBalance
Notes: delete

## Slide 7
iFThings App
iFBalance
https://play.google.com/store/apps/details?id=com.indifrog.ifthings
https://apps.apple.com/kr/app/ifthings/id1552208956

## Slide 8
BMP388
Pressure Sensor
200 ~ 1250 hPa
30cm Error
I2C
200Hz Sampling
ESP32 PICO V3
Xtensa® Dual Core 32-bit CPU
WiFi 2.4 GHz
Bluetooth
4 MB Flash Memory
34 programmable GPIOs
12 bit SAR ADC x 18
RTC
MPU9250
Triple Axis MEMS
Accelerometer 3 Axis
Gyroscope 3 Axis
Magnetometer 3 Axis
400KHz Fast Mode I2C
Digital Motion Processing
CP2102
USB2Serial
300 ~ 921600 bps
Development Tools
Arduino
PlatformIO
Native
RESET Button
GPIO 0 Button
iFZero Board
iFBalance

## Slide 9
iFBalance
Environment Setup

## Slide 10
Code it!!
1. Arduino
https://www.arduino.cc/en/Main/Software
2. Visual Studio Code
iFBalance
https://code.visualstudio.com/

## Slide 11
Install Visual Studio Code
&
PlatformIO
iFBalance

## Slide 12
Code in Visual Studio Code
&
PlatformIO
iFBalance

## Slide 13
Code in Visual Studio Code
&
PlatformIO
iFBalance

## Slide 14
Add a Library
in
PlatformIO
iFBalance

## Slide 15
Configure PlatformIO.ini
iFBalance
[env:pico32]
platform = espressif32
board = pico32
framework = arduino
; ///// 추가함 ////// by serimo 2020.07.25
upload_speed = 921600
monitor_speed = 115200
monitor_port = COM9 ; Windows
; monitor_port = /dev/cu.SLAB_USBtoUART. ; Mac
lib_deps =
# RECOMMENDED
# Accept new functionality in a backwards compatible manner and patches
makuna/NeoPixelBus @ ^2.6.0
# Accept only backwards compatible bug fixes
# (any version with the same major and minor versions, and an equal or greater patch version)
makuna/NeoPixelBus @ ~2.6.0
# The exact version
makuna/NeoPixelBus @ 2.6.0
Automatic

## Slide 16
Upload a Program
in
PlatformIO
iFBalance
Compile
Upload
Serial
Monitor

## Slide 17
iFBalance
1st Program
Blink LED
https://github.com/ShantanuSen/KookminSeminar/tree/main/LED%20Blinking

## Slide 18
iFZero Board GPIO Connection
IR_LEFT_L
Battery
IR_CENTER_LB
IR_CENTER_LF
IR_CENTER_RF
IR_CENTER_C
IR_CENTER_RB
I2C SDA
I2C SCL
I38
GND
IO21
TX
RX
IO22
IO19
GND
IO20
VSD
IO5
CMD
IO4
GND
S3
S2
IO8
IO7
CLK
I37
I36
I39
I34
I35
IO32
IO33
IO25
IO26
IO27
IO14
IO12
GND
IO13
IO15
IO0
IO2
5V
3V3
3V3
EN
IO4 ( BLUE LED )
E_LEFT_A
M_RIGHT_B
M_RIGHT_F
E_LEFT_B
E_RIGHT_A
E_RIGHT_B
Button
COLOR_LED
IR_RIGHT_R
IR_TR_1
IR_TR_2
IR_TR_3
M_LEFT_B
M_LEFT_F
TOF_INT
IR_LEFT_L IR_CENTER_C IR_RIGHT_R
IR_CENTER_LB IR_CENTER_RF
IR_CENTER_LF IR_CENTER_RB
iFBalance

## Slide 19
iFBalance
RGB LED

## Slide 20
iFBalance
Color LED (SK6812)
GPIO_2

## Slide 21
iFBalance
Color LED (SK6812)
In iFBalance
4 RGB LED

## Slide 22
iFBalance
Color LED (SK6812)
LED 1
LED 3
LED 4
LED 2

## Slide 23
iFBalance
Control SK6812 (NeoPixelBus)
RgbColor red(colorSaturation, 0, 0);
RgbColor green(0, colorSaturation, 0);
RgbColor blue(0, 0, colorSaturation);
RgbColor white(colorSaturation);
RgbColor black(0);
Define Color Brightness
int c = ++nPixel % 4;
strip.SetPixelColor(0, c==0? blue : black);
strip.SetPixelColor(1, c==1? green : black);
strip.SetPixelColor(2, c==2? red : black);
strip.SetPixelColor(3, c==3? blue : black);
strip.Show(); // Send the updated pixel colors to the hardware.
Set color to each LED

## Slide 24
iFBalance
2nd Program
Control RGB LED
https://github.com/ShantanuSen/KookminSeminar/tree/main/Color%20LED_Part%201%20(Basic)

## Slide 25
iFBalance
Real Time Operating System (RTOS)

## Slide 26
iFBalance
Free RTOS
Several things concurrently

## Slide 27
iFBalance
Free RTOS
Task: set of program instructions loaded in memory
Thread: unit of CPU utilization with its own program counter and stack
Process: instance of a computer program
FreeRTOS: Task = Thread

## Slide 28
iFBalance
Super Loop
Setup
Task 1
Task 2
Task 3
Loop
Entry Point (main())

## Slide 29
iFBalance
Interrupt
Setup
Task 1
Task 2
Task 3
Loop
Entry Point (main())
Interrupt Service Routine
(ISR)

## Slide 30
iFBalance
RTOS
Entry Point (main())
Setup
Task C
Task B
Task A

## Slide 31
Primary
Core
(Run OS )
Secondary Core
Secondary Core
Secondary Core
Asymmetric multiprocessing (AMP)
Primary
Core
(Run OS )
Primary
Core
(Run OS )
Primary
Core
(Run OS )
Primary
Core
(Run OS )
Symmetric multiprocessing (SMP)
Free RTOS

## Slide 32
AMP vs SMP
One core is primary core
Others are secondary
Primary core runs operating system (OS)
Cores may not be same architecture
AMP
SMP
Every core is primary core
Every core runs operating system (OS)
Cores are same architecture

## Slide 33
DMA
Core 0
Cache
Embedded
Memory
Core 1
Cache
MMU
External
Memory
Peripheral
32KB
32KB
0
1
PRO CPU
APP CPU
Interrupts
Interrupts
Scheduler
Scheduler
Task A

## Slide 34
iFBalance
Free RTOS
void taskToggleBlueLED(void *pvParameter) {
portTickType delay = *(portTickType*)pvParameter;
digitalWrite(pinBlueLED, LOW);
vTaskDelay(delay/portTICK_PERIOD_MS);
}
1 ms
Create a Task
non-blocking

## Slide 35
iFBalance
Free RTOS
Assign a Task
xTaskCreatePinnedToCore (taskToggleBlueLED, // function to be called
"Toggle Blue LED",, // name of task
1024, // stack size(in bytes)
(void*)&timeDelay, // param. To pass to function
        uxTaskPriorityGet(NULL), //task priority
        &TaskHandle, //task handle
        0); // core number

## Slide 36
iFBalance
Free RTOS
Task Scheduling
time
Task A
Task A
Task A
Task C
Task B
Idle
Task C
Task A
OS
0
1
Priority
(S/W)
ISR
(H/W)
“Preemptive Scheduling”

## Slide 37
iFBalance
Free RTOS
Task States
Ready
Running
Blocked
Suspended
Task
Creation
vTaskSuspend()
vTaskResume()
Event
Blocking API
Function called
vTaskSuspend()
vTaskSuspend()

## Slide 38
iFBalance
Free RTOS
Race Condition
void incTask(void *parameters) {
int local_var;
while(1) {
local_var = shared_var;
local_var ++;
vTaskDelay(500 / portTICK_PERIOD_MS);
shared_var = local_var;
Serial.println(shard_var);
}
}
Global variable
critical
section

## Slide 39
iFBalance
Free RTOS
Before Mutex

## Slide 40
iFBalance
Free RTOS
After Mutex

## Slide 41
iFBalance
Free RTOS
Mutual Exclusion (MUTEX)
void incTask(void *parameters) {
int local_var;
while(1) {
// take mutex prior to critical section
if (xSemaphoreTake (mutex, 0) == pdTRUE) {
  local_var = shared_var;
  local_var ++;
  vTaskDelay(500 / portTICK_PERIOD_MS);
  shared_var = local_var;
  // give mutex prior to critical section
  xSemaphoreGive (mutex);
  Serial.println(shared_var);
}
}
static SemaphoreHandle_t mutex;

## Slide 42
iFBalance
3rd Program
Play with onboard Blue LED using FreeRTOS
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(LED%20Blink)

## Slide 43
iFBalance
Free RTOS
Blink LED from Protocol CPU
xTaskCreatePinnedToCore( // Use xTaskCreate() in vanilla FreeRTOS
taskToggleBlueLED, // Function to be called
"Toggle BLUE LED", // Name of task
1024, // Stack size (bytes in ESP32, words in FreeRTOS)
(void*)&timeDelay, // Parameter to pass to function
uxTaskPriorityGet(NULL), // Task priority (0 to configMAX_PRIORITIES - 1)
&taskHandle, // Task handle
PRO_CPU); // core No.

## Slide 44
iFBalance
Free RTOS
Blink LED from Protocol & Application CPU
xTaskCreatePinnedToCore(taskToggleBlueLED2,
"Toggle Blue LED2",
1024,
(void*)&timeDelay2,
uxTaskPriorityGet(NULL),
&taskHandle,
APP_CPU); // change to PRO_CPU. What will happen?
xTaskCreatePinnedToCore( // Use xTaskCreate() in vanilla FreeRTOS
taskToggleBlueLED, // Function to be called
"Toggle BLUE LED", // Name of task
1024, // Stack size (bytes in ESP32, words in FreeRTOS)
(void*)&timeDelay, // Parameter to pass to function
uxTaskPriorityGet(NULL), // Task priority (0 to configMAX_PRIORITIES - 1)
&taskHandle, // Task handle
PRO_CPU); // core No.

## Slide 45
iFBalance
4th Program
Create LED Class
&
Use with FreeRTOS
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(LED%20Class)

## Slide 46
iFBalance
5th Program
LED, Button, & FreeRTOS
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(HW%20ISR)

## Slide 47
iFBalance
6th Program
LED Flash witn Button, & FreeRTOS
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(HW%20ISR)

## Slide 48
iFBalance
7th Program
NeoPixel Class, & FreeRTOS
https://github.com/ShantanuSen/KookminSeminar/tree/main/Color%20LED_Part%202%20(FreeRTOS)

## Slide 49
iFBalance
DC Motor Control

## Slide 50
iFBalance
DC Motor
Left Motor
Right Motor

## Slide 51
iFBalance
Motor Control GPIO
LEFT_WHEEL_FORWARD IO7
LEFT_WHEEL_BACKWARD IO8
RIGHT_WHEEL_FORWARD IO27
RIGHT_WHEEL_BACKWARD IO26
DC Motor

## Slide 52
iFBalance
Pulse Width Modulation
(PWM)

## Slide 53
iFBalance
8th Program
Control DC Motor
https://github.com/ShantanuSen/KookminSeminar/tree/main/Color%20LED_Part%202%20(FreeRTOS)

## Slide 54
iFBalance
Encoder

## Slide 55
iFBalance
Encoder
Rotary movements  electrical signals
Absolute encoder | Incremental encoder
Computer mouse wheel, flow meter, conveyor belt, printer

## Slide 56
iFBalance
Encoder Types
Single Output
2-Bit Quadrature Output

## Slide 57
iFBalance
Encoder Technologies
Technology
Contact
Optical
Inductive
Magnetic

## Slide 58
iFBalance
Encoder
N
S
Hall Sensor
Hall Sensor
A
B
1
1
1
1
0
0
0
0

## Slide 59
iFBalance
Encoder
How to Calculate speed from encoder?
for left motor:
countLeft += (lastLeftA  newLeftB) – (newLeftA  lastLeftB)
Pin 1 (A) | Pin 2 (B) | Direction
H (Last) | H (Last) | 
L (New) | H (New) | HH – LH = 0 – 1 = -1
L | L | LL – LH = 0 – 1 = -1
H | L | LL – HL = 0 – 1 = -1

## Slide 60
iFBalance
Encoder, PWM, RPM
Bharat Joshi, Rakesh Shrestha, Ramesh Chaudhary. “Modeling, Simulation and Implementation of Brushed DC Motor Speed Control Using Optical Incremental Encoder Feedback”, Proceedings of IOE Graduate Conference, 2014
In Ideal State,
Sampling frequency
Revolutions per minute
No. of Poles
Pulses per revolution
(Encoder resolution)
Nominal diameter of wheel (mm)
Gear ratio
Notes: Not Sure

## Slide 61
iFBalance
Encoder
Encoder Pin GPIO
LEFT_A IO25
LEFT_B IO14
RIGHT_A IO13
RIGHT_B IO15

## Slide 62
iFBalance
Encoder Interrupt
attachInterrupt(m_nLeA, leftISR, CHANGE);
attachInterrupt(m_nLeB, leftISR, CHANGE);
attachInterrupt(m_nReA, rightISR, CHANGE);
attachInterrupt(m_nReB, rightISR, CHANGE);
Interrupt attach to hardware pin

## Slide 63
iFBalance
Encoder Interrupt
void IRAM_ATTR iFEncoder::leftISR()
{
bool newLeftB, newLeftA;
portENTER_CRITICAL (& muxl);
newLeftB = digitalRead (m_nLeB);
newLeftA = digitalRead (m_nLeA); countLeft += (lastLeftA ^ newLeftB) - (newLeftA ^ lastLeftB);
if ((lastLeftA ^ newLeftA) & (lastLeftB ^ newLeftB)) {
errorLeft = true;
}
lastLeftA = newLeftA;
lastLeftB = newLeftB;
portEXIT_CRITICAL(&muxl);
}
Interrupt Service Routine (ISR)

## Slide 64
iFBalance
9th Program
Calculate speed from encoder output
https://github.com/ShantanuSen/KookminSeminar/tree/main/Color%20LED_Part%202%20(FreeRTOS)

## Slide 65
iFBalance
Motion Processing Unit (MPU)

## Slide 66
INS ( Inertial Navigation System )
( Attitude & Heading Reference System )
Altimeter
GPS ( Global Positioning System )
Barometer
ToF
UltraSonic
Lidar
Optical Flow
IMU
Accelerometers
Gyroscopes
( Inertial Measurement Unit )
+
AHRS
MRAG
( Magnetic, Anglear Rate, Gravity )
Compass
Magnetometers
MPU9250
BMP388
VL53L3CX
iFBalance
iFBalance

## Slide 67
MPU9250 : IMU Sensor
iFBalance
Notes: Roll direction change from original blog

## Slide 68
MPU9250 : IMU Sensor
iFBalance
MPU Pin GPIO
I2C SDA IO21
I2C SCL IO22
MPU9250 Interrupt IO5
Notes: Roll direction change from original blog

## Slide 69
MPU9250 : IMU Sensor
Front
Back
Pitch + Offset
Setpoint
0
Pitch
Roll
Yaw
iFBalance
Notes: Roll direction change from original blog

## Slide 70
Pitch
Roll
Yaw
iFBalance

## Slide 71
iFBalance
10th Program
Accelerometer, Gyroscope, & Magnetometer data from MPU9250
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(HW%20ISR)

## Slide 72
iFBalance
Proportional Integral Derivative (PID)

## Slide 73
PID Control
iFBalance
Proportional
Integration
Differentiation

## Slide 74
Closed Loop Control
iFBalance
- The current output status is reflected in the control
control by reflecting the difference between the set point () and the robot pitch ()
Opened Loop Control
Controller
Process
- It does not reflect the current output status
r(t)
u(t)
y(t)
Process
Controller
Sensor
r(t)
u(t)
y(t)
e(t)
Error
Control signal
Output
Reference
Measured value

## Slide 75
iFBalance
PID Control
Proportional
Integration
Differentiation
∝ error
steady state error
Overshoot Stability

## Slide 76
iFBalance
PID Control
GIF credit: https://commons.wikimedia.org/wiki/File:PID_Compensation_Animated.gif

## Slide 77
iFBalance
PID Control
Set
Set 𝑘_𝑝
Set & = 0
Set 𝑘_𝑖 & 𝑘_𝑑 = 0
Set
Set 𝑘_𝑖
Fixed
Fixed 𝑘_𝑝
Set
Set 𝑘_𝑑
Fixed & Fixed
Fixed 𝑘_𝑝 & Fixed 𝑘_𝑖
Start from (–) pitch value
Stop at (+) pitch value
Increase
Increase 𝑘_𝑝
is set
𝑘_𝑝 is set
Increase
Increase 𝑘_𝑖
Pitch repeats between (+) & (-)
Stop at uniform vibration
Stop 𝑘_𝑖 at uniform vibration
Stop at minimum overshoot

## Slide 78
iFBalance
P
I
D
e(t)
Setpoint
Pitch
Process
Proportional
Integral
Differential
IMU Sensor
PWM Motor Control
y(t)
u(t)
r(t)
PID Controller
Measured value
Reference

## Slide 79
PID Control
iFBalance
Proportional
Integral
Differential
P
I
D
Error
Setpoint
Output
Pitch
Front
Back
Pitch + Offset
Setpoint
0
Output
Measurement
iFBalance
IMU Sensor
PWM Motor Control
Time Interval ( Unit : Second ) : 0.005 sec
Input
System
System Variable

## Slide 80
iFBalance
PID
Setpoint
Output
Pitch
Measurement
Input
System
Mixer
Left
Right

## Slide 81
iFBalance
PID
Setpoint
Output
Pitch
Measurement
Input
System
PID
Setpoint
Output
Pitch
Measurement
Input

## Slide 82
iFBalance
PID Control
Ziegler–Nichols method
 Heuristic PID control method
https://en.wikipedia.org/wiki/Ziegler%E2%80%93Nichols_method

## Slide 83
iFBalance
11th Program
Speed control with PID
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(HW%20ISR)

## Slide 84
iFBalance
Time of Flight (ToF) Sensor

## Slide 85
Time of Flight (ToF)
iFBalance
Field-of-View (FoV): 27 °
Time-of-Flight (ToF)
Laser-ranging sensor
2 Meter
I2C

## Slide 86
300+ mm Detection
FoV 25º
Multi Target Detection
VL53L3CX

## Slide 87
iFBalance

## Slide 88
Chip On/Off

## Slide 90
iFBalance
12th Program
Measure Distance Using ToF Sensor
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(HW%20ISR)

## Slide 91
IR Sensor Module

## Slide 92
ESP 32 ADC  Group 1
ADC1 Channels GPIO
Channel 0 IO36
Channel 1 IO37
Channel 2 IO38
Channel 3 IO39
Channel 4 IO32
Channel 5 IO33
Channel 6 IO34
Channel 7 IO35

## Slide 93
IR Sensor Position
Left Most
Left Back
Left Front
Right Most
Right Font
Right Back
Center

## Slide 94
IR Sensor Pair  GPIO
Sensor Location GPIO
Left Most (LL) GPIO5
Center (CC) GPIO5
Right Most (RR) GPIO5
Left Back GPIO4
Right Front GPIO4
Left Front GPIO20
Right Back GPIO20
Group 1
Group 2
Group 3

## Slide 95
iFBalance
13th Program
Read IR Sensor Module
https://github.com/ShantanuSen/KookminSeminar/tree/main/Free%20RTOS%20Basic%20(HW%20ISR)

## Slide 97
https://blog.naver.com/serimo/222007740015
1cm
iFBalance
Line Track Specification and IR Sensor Placement