## Slide 1: iFBalance Robot
Shantanu Sen Gupta
Manager, Research Institute
www.koreaits.com
STEAM AI Education Platform
(주)인디프로그

## Slide 2
iFBalance
+
AI
Notes: delete

## Slide 3
iFBalance
iFBalance Components
Environment Setup
RGB LED Control
DC Motor Control
Encoder
Motion Processing Unit (MPU) Sensor
Time of Flight (ToF) Sensor
Proportional, Derivative, and Integral (PID) Control System
IR Sensor Module
Contents
Notes: delete

## Slide 4
iFBalance
Day1
- Components - Coding - RGB LED - RTOS
Day 3
- IMU - ToF
Day 4
- PID - IR
Day 2
- Motor - Encoder
Notes: delete

## Slide 5
iFBalance
1.0 Components of iFBalance

## Slide 6
Features
iFBalance

## Slide 7
iFBalance

## Slide 8
iFZero Module
iFBalance
Notes: delete

## Slide 9
iFThings App
iFBalance
https://play.google.com/store/apps/details?id=com.indifrog.ifthings
https://apps.apple.com/kr/app/ifthings/id1552208956

## Slide 10
BMP388
Pressure Sensor
200 ~ 1250 hPa
30cm Error
I2C
200Hz Sampling
ESP32 PICO V3
Xtensa® Dual Core 32-bit CPU
WiFi 2.4 GHz
Bluetooth
4 MB Flash Memory
34 programmable GPIOs
12 bit SAR ADC x 18
RTC
MPU9250
Triple Axis MEMS
Accelerometer 3 Axis
Gyroscope 3 Axis
Magnetometer 3 Axis
400KHz Fast Mode I2C
Digital Motion Processing
CP2102
USB2Serial
300 ~ 921600 bps
Development Tools
Arduino
PlatformIO
Native
RESET Button
GPIO 0 Button
iFZero Board
iFBalance

## Slide 11
iFBalance
2.0 Environment Setup

## Slide 12
Code it!!
1. Arduino
https://www.arduino.cc/en/Main/Software
2. Visual Studio Code
iFBalance
https://code.visualstudio.com/

## Slide 13
Install Visual Studio Code
&
PlatformIO
iFBalance

## Slide 14
iFBalance
Code in Visual Studio Code
&
PlatformIO

## Slide 15
iFBalance
Arduino Code Structure
In ESP-IDF,
void main_app()
In ESP-IDF,
void loopTask()

## Slide 16
iFBalance
Add a Library

## Slide 17
iFBalance
[env:pico32]
platform = espressif32
board = pico32
framework = arduino
; ///// 추가함 ////// by serimo 2020.07.25
upload_speed = 921600
monitor_speed = 115200
monitor_port = COM9 ; Windows
; monitor_port = /dev/cu.SLAB_USBtoUART. ; Mac
lib_deps =
# RECOMMENDED
# Accept new functionality in a backwards compatible manner and patches
makuna/NeoPixelBus @ ^2.6.0
# Accept only backwards compatible bug fixes
# (any version with the same major and minor versions, and an equal or greater patch version)
makuna/NeoPixelBus @ ~2.6.0
# The exact version
makuna/NeoPixelBus @ 2.6.0
Automatic
Configure Platform.ini

## Slide 18
iFBalance
Compile
Upload
Serial
Monitor
Upload a Program

## Slide 19
iFZero Board GPIO Connection
IR_LEFT_L
Battery
IR_CENTER_LB
IR_CENTER_LF
IR_CENTER_RF
IR_CENTER_C
IR_CENTER_RB
I2C SDA
I2C SCL
I38
GND
IO21
TX
RX
IO22
IO19
GND
IO20
VSD
IO5
CMD
IO4
GND
S3
S2
IO8
IO7
CLK
I37
I36
I39
I34
I35
IO32
IO33
IO25
IO26
IO27
IO14
IO12
GND
IO13
IO15
IO0
IO2
5V
3V3
3V3
EN
IO4 ( BLUE LED )
E_LEFT_A
M_RIGHT_B
M_RIGHT_F
E_LEFT_B
E_RIGHT_A
E_RIGHT_B
Button
COLOR_LED
IR_RIGHT_R
IR_TR_1
IR_TR_2
IR_TR_3
M_LEFT_B
M_LEFT_F
TOF_INT
IR_LEFT_L IR_CENTER_C IR_RIGHT_R
IR_CENTER_LB IR_CENTER_RF
IR_CENTER_LF IR_CENTER_RB
iFBalance

## Slide 20
iFBalance
1st Program
Blink LED
Indigrog Blog (Blink LED Code)

## Slide 21
iFBalance
3.0 RGB LED

## Slide 22
iFBalance
Color LED (SK6812)
In iFBalance
4 RGB LED

## Slide 23
iFBalance
LED 1
LED 3
LED 4
LED 2
Color LED (SK6812)

## Slide 24
iFBalance
RgbColor red(colorSaturation, 0, 0);
RgbColor green(0, colorSaturation, 0);
RgbColor blue(0, 0, colorSaturation);
RgbColor white(colorSaturation);
RgbColor black(0);
Define Color Brightness
int c = ++nPixel % 4;
strip.SetPixelColor(0, c==0? blue : black);
strip.SetPixelColor(1, c==1? green : black);
strip.SetPixelColor(2, c==2? red : black);
strip.SetPixelColor(3, c==3? blue : black);
strip.Show(); // Send the updated pixel colors to the hardware.
Set color to each LED
Color LED (SK6812)
NeoPixelBus

## Slide 25
iFBalance
2nd Program
Control RGB LED
Indifrog Blog (Control RGB LED)

## Slide 26
iFBalance
4.0 Real Time Operating System (RTOS)

## Slide 27
iFBalance
General purpose operating system (GPOS)
 Windows, Linux, MacOS
 Not suitable for critical application
 Variable interrupt latency
 Not follow programmed priorities strictly
Real time operating system (RTOS)
 FreeRTOS, Embedded Linux
 Suitable for critical application
 Fixed interrupt latency
 Follow programmed priorities strictly
Free RTOS

## Slide 28
iFBalance
Task: set of program instructions loaded in memory
Thread: unit of CPU utilization with its own program counter and stack
Process: instance of a computer program
Free RTOS
ESP32 has separate Free RTOS, ESP-IDF Free RTOS
Basic Free RTOS is called Vanilla Free RTOS

## Slide 29
iFBalance
Setup
Task 1
Task 2
Task 3
Loop
Entry Point (main())
Loop

## Slide 30
iFBalance
Hardware Interrupt
Interrupt Service Routine
(ISR)
Setup
Task 1
Task 2
Task 3
Loop
Entry Point (main())

## Slide 31
iFBalance
Entry Point (main())
Setup
 Task C
 Task B
 Task A
RTOS

## Slide 32
DMA
Core 0
Cache
Embedded
Memory
Core 1
Cache
MMU
External
Memory
Peripheral
32KB
32KB
0
1
PRO CPU
APP CPU
Interrupts
Interrupts
Scheduler
Scheduler
Task A
ESP32 System Architecture

## Slide 33
iFBalance
Task Scheduling
time
Task A
Task A
Task A
Task C
Task B
Idle
Task C
Task A
OS
0
1
Priority
(S/W)
ISR
(H/W)
“Preemptive Scheduling”
Free RTOS

## Slide 34
iFBalance
Create a Task
Free RTOS
// Task to be created.
void vTaskCode( void * pvParameters )
{
for( ;; )
{
// Task code goes here.
}
}

## Slide 35
iFBalance
void taskToggleBlueLED(void *pvParameter) {
portTickType delay = *(portTickType*)pvParameter;
digitalWrite(pinBlueLED, LOW);
vTaskDelay(delay/portTICK_PERIOD_MS);
}
1 ms
Create a Task
non-blocking
Free RTOS

## Slide 36
iFBalance
Assign a Task
Free RTOS
BaseType_t xTaskCreatePinnedToCore (TaskFunction_t pvTaskCode,
const char *constpcName,
const uint32_t usStackDepth,
void *constpvParameters,
UBaseType_t uxPriority,
TaskHandle_t *constpvCreatedTask,
const BaseType_t xCoreID)
pvTaskCode  Pointer to a task function
constpcName  Task name
usStackDepth  Stacksize in bytes
constpvParameters  Parameters to pass in task function
uxPriority  Set priority level
constpvCreatedTask  Task handler of the created task
xCoreID  Core ID where the task will be run

## Slide 37
iFBalance
Assign a Task
xTaskCreatePinnedToCore (taskToggleBlueLED, // function to be called
"Toggle Blue LED",, // name of task
1024, // stack size(in bytes)
(void*)&timeDelay, // param. To pass to function
uxTaskPriorityGet(NULL), //task priority
&TaskHandle, //task handle
0); // core number
Free RTOS

## Slide 38
iFBalance
Task States
Free RTOS
Running
Create Task
Suspended
vTaskSuspend()
vTaskResume()

## Slide 39
iFBalance
Task States
Free RTOS
void vTaskDelete(TaskHandle_txTaskToDelete)
UBaseType_t uxTaskPriorityGet(constTaskHandle_txTask)
void vTaskSuspend(TaskHandle_txTaskToSuspend)
void vTaskResume(TaskHandle_txTaskToResume)
Remove a task from the RTOS real time kernel’s management. The task being deleted will be removed from all ready, blocked, suspended and event lists
Resumes a suspended task
Suspend any task. When suspended a task will never get any microcontroller processing time, no matter what its priority.
Obtain the priority of any task

## Slide 40
iFBalance
3rd Program
Play with onboard Blue LED using FreeRTOS
Indifrog Blog (Free RTOS Basic)

## Slide 41
iFBalance
Blink LED from Protocol CPU
xTaskCreatePinnedToCore( // Use xTaskCreate() in vanilla FreeRTOS
taskToggleBlueLED, // Function to be called
"Toggle BLUE LED", // Name of task
1024, // Stack size (bytes in ESP32, words in FreeRTOS)
(void*)&timeDelay, // Parameter to pass to function
uxTaskPriorityGet(NULL), // Task priority (0 to configMAX_PRIORITIES - 1)
&taskHandle, // Task handle
APP_CPU); // core No.
Free RTOS

## Slide 42
iFBalance
Blink LED from 2 Tasks
xTaskCreatePinnedToCore(taskToggleBlueLED2,
"Toggle Blue LED2",
1024,
(void*)&timeDelay2,
uxTaskPriorityGet(NULL),
&taskHandle,
APP_CPU); // change to PRO_CPU. What will happen?
xTaskCreatePinnedToCore( // Use xTaskCreate() in vanilla FreeRTOS
taskToggleBlueLED, // Function to be called
"Toggle BLUE LED", // Name of task
1024, // Stack size (bytes in ESP32, words in FreeRTOS)
(void*)&timeDelay, // Parameter to pass to function
uxTaskPriorityGet(NULL), // Task priority (0 to configMAX_PRIORITIES - 1)
&taskHandle, // Task handle
APP_CPU); // core No.
Free RTOS

## Slide 43
iFBalance
Race Condition
void incTask(void *parameters) {
int local_var;
while(1) {
local_var = shared_var;
local_var ++;
vTaskDelay(500 / portTICK_PERIOD_MS);
shared_var = local_var;
Serial.println(shard_var);
}
}
Global variable
critical
section
Free RTOS

## Slide 44
iFBalance
Before Mutex
Free RTOS

## Slide 45
iFBalance
After Mutex
Free RTOS

## Slide 46
iFBalance
MUTEX vs Semaphore
Free RTOS
MUTEX | Semaphore
Allows multiple process threads to access a single shared resource but only one at a time | Allows multiple process threads to access the finite instance of the resource until available
For example, a 4kB buffer can be accessed by only one process at a time | For example, a 4 kB buffer can be split into four 1kB buffers. A semaphore can be associated with these four buffers

## Slide 47
iFBalance
MUTEX
Free RTOS
xSemaphoreGive(xSemaphore)
xSemaphoreCreateMutex()
xSemaphoreTake(xSemaphore, xBlockTime)
Macro to release a semaphore
Macro to obtain a semaphore.
Creates a new mutex type semaphore instance, and returns a handle by which the new mutex can be referenced.

## Slide 48
iFBalance
Mutual Exclusion (MUTEX)
void incTask(void *parameters) {
int local_var;
while(1) {
// take mutex prior to critical section
if (xSemaphoreTake (mutex, 0) == pdTRUE) {
  local_var = shared_var;
  local_var ++;
  vTaskDelay(500 / portTICK_PERIOD_MS);
  shared_var = local_var;
  // give mutex prior to critical section
  xSemaphoreGive (mutex);
  Serial.println(shared_var);
}
}
static SemaphoreHandle_t mutex;
Free RTOS

## Slide 49
iFBalance
Special Program
Increase a variable from two task

## Slide 50
iFBalance
4th Program
Create LED Class
FreeRTOS
Indifrog Blog (iFLED Class for onboard LED)

## Slide 51
iFBalance
Special MUTEX
Free RTOS
portENTER_CRITICAL(&spinlock);
// Do something here
portEXIT_CRITICAL(&spinlock);
A spinlock is required in order to prevent multiple CPUs from accessing the same resource concurrently

## Slide 52
iFBalance
5th Program
LED, Button
FreeRTOS
Indifrog Blog (HW ISR)

## Slide 53
iFBalance
6th Program
LED Blink with Button FreeRTOS
Indifrog Blog (LED Blink with Button FREE RTOS)

## Slide 54
iFBalance
7th Program
NeoPixel Class FreeRTOS
Indifrog Blog (iFLED wrapper Class)

## Slide 55
iFBalance
5.0 DC Motor Control

## Slide 56
iFBalance
DC Motor Working Principle

## Slide 57
iFBalance
DC Motor
Left Motor
Right Motor

## Slide 58
iFBalance
H-Bridge Operation

## Slide 59
iFBalance
H-Bridge Operation
S1 | S2 | S3 | S4 | Result
1 | 0 | 0 | 1 | Motor moves right
0 | 1 | 1 | 0 | Motor moves left
0 | 0 | 0 | 0 | Motor Idle
1 | 0 | 0 | 0 | 
0 | 1 | 0 | 0 | 
0 | 0 | 1 | 0 | 
0 | 0 | 0 | 1 | 
0 | 1 | 0 | 1 | Motor brakes
1 | 0 | 1 | 0 | 
× | × | 1 | 1 | Short circuit
1 | 1 | × | × | 

## Slide 60
iFBalance
Pulse Width Modulation
(PWM)

## Slide 61
iFBalance
Pulse Width Modulation
(PWM)

## Slide 62
iFBalance
DC Motor Controller
(DRV8833)

## Slide 63
iFBalance
Motor Control GPIO
LEFT_WHEEL_FORWARD IO7
LEFT_WHEEL_BACKWARD IO8
RIGHT_WHEEL_FORWARD IO27
RIGHT_WHEEL_BACKWARD IO26
DC Motor

## Slide 64
iFBalance
PWM Function in ESP32
ledcWrite(Channel, dutyCycle);
ledcSetup(Channel, freq, resolution);
ledcAttachPin(GPIOPin, Channel);
changing the GPIO output value with PWM
attach the channel to the GPIO to be controlled
configure PWM functionalitites. 18 channles are available in two ADC group. ADC1_CHx (0~7) & ADC2_CHx (0~9)
Maximum resolution 16 bit.
DC Motor

## Slide 65
iFBalance
8th Program
Control DC Motor
Indifrog Blog (DC Motor Control)

## Slide 66
iFBalance
6.0 Encoder

## Slide 67
iFBalance
Encoder
Rotary movements  electrical signals
Absolute encoder | Incremental encoder
Computer mouse wheel, flow meter, conveyor belt, printer

## Slide 68
iFBalance
Single Output
2-Bit Quadrature Output
Encoder

## Slide 69
iFBalance
Technology
Contact
Optical
Inductive
Magnetic
Encoder

## Slide 70
iFBalance
N
S
Hall Sensor
Hall Sensor
A
B
1
1
1
1
0
0
0
0
Channel A
Channel B
Encoder

## Slide 71
iFBalance
How to Calculate speed from encoder?
for left motor:
countLeft += (lastLeftA  newLeftB) – (newLeftA  lastLeftB)
Pin 1 (A) | Pin 2 (B) | Direction
H (Last) | H (Last) | 
L (New) | H (New) | HH – LH = 0 – 1 = -1
L | L | LL – LH = 0 – 1 = -1
H | L | LL – HL = 0 – 1 = -1
Encoder

## Slide 72
iFBalance
Encoder Pin GPIO
LEFT_A IO25
LEFT_B IO14
RIGHT_A IO13
RIGHT_B IO15
Encoder

## Slide 73
iFBalance
attachInterrupt(m_nLeA, leftISR, CHANGE);
attachInterrupt(m_nLeB, leftISR, CHANGE);
attachInterrupt(m_nReA, rightISR, CHANGE);
attachInterrupt(m_nReB, rightISR, CHANGE);
Interrupt attach to hardware pin
Encoder

## Slide 74
iFBalance
void IRAM_ATTR iFEncoder::leftISR()
{
bool newLeftB, newLeftA;
portENTER_CRITICAL (& muxl);
newLeftB = digitalRead (m_nLeB);
newLeftA = digitalRead (m_nLeA); countLeft += (lastLeftA ^ newLeftB) - (newLeftA ^ lastLeftB);
if ((lastLeftA ^ newLeftA) & (lastLeftB ^ newLeftB)) {
errorLeft = true;
}
lastLeftA = newLeftA;
lastLeftB = newLeftB;
portEXIT_CRITICAL(&muxl);
}
Interrupt Service Routine (ISR)
Encoder

## Slide 75
iFBalance
9th Program
Calculate speed from encoder output
Indifrog Blog (Encoder)

## Slide 76
iFBalance
6. Motion Processing Unit (MPU)

## Slide 77
INS ( Inertial Navigation System )
( Attitude & Heading Reference System )
Altimeter
GPS ( Global Positioning System )
Barometer
ToF
UltraSonic
Lidar
Optical Flow
IMU
Accelerometers
Gyroscopes
( Inertial Measurement Unit )
+
AHRS
MRAG
( Magnetic, Anglear Rate, Gravity )
Compass
Magnetometers
MPU9250
BMP388
VL53L3CX
iFBalance
iFBalance

## Slide 78
MPU9250 : IMU Sensor
iFBalance
6 axis IMU(Inertial Measurement Unit) sensor(Accelerometers, Gyroscopes) : MPU6500
3-Axis Magnetometers Sensor : AK8963
Operates at 3.3V
I2C, SPI support
Application
  AHRS(Attitude & Heading Reference System) 혹은 MARGS(Magnetic, Angular Rate, Gravity)
  DMP(Digital Motion Processing)
  Digital Compass
Notes: Roll direction change from original blog

## Slide 79
MPU9250 : IMU Sensor
iFBalance

## Slide 80
MPU9250 : IMU Sensor
iFBalance
MPU Pin GPIO
I2C SDA IO21
I2C SCL IO22
MPU9250 Interrupt IO5

## Slide 81
Accelerometer
iFBalance
Digital-output triple-axis accelerometer with a programmable full scale
range of ±2g, ±4g, ±8g and ±16g and integrated 16-bit ADCs
Accelerometer normal operating current: 450µA
Low power accelerometer mode current: 8.4µA at 0.98Hz, 19.8µA at
31.25Hz
Sleep mode current: 8µA
User-programmable interrupts
Wake-on-motion interrupt for low power operation of applications
processor
Self-test

## Slide 82
Gyroscope
iFBalance
Digital-output X-, Y-, and Z-Axis angular rate sensors (gyroscopes) with a
user-programmable full scale range of ±250, ±500, ±1000, and ±2000°/sec and integrated 16-bit ADCs
Digitally-programmable low-pass filter
Gyroscope operating current: 3.2mA
Sleep mode current: 8µA
Factory calibrated sensitivity scale factor
Self-test

## Slide 83
Magnetometer
iFBalance
3-axis silicon monolithic Hall-effect magnetic sensor with magnetic concentrator
Wide dynamic measurement range and high resolution with lower current
consumption.
Output data resolution of 14 bit (0.6µT/LSB)
Full scale measurement range is ±4800µT
Magnetometer normal operating current: 280µA at 8Hz repetition rate
Self-test function with internal magnetic source to confirm magnetic sensor operation
on end products

## Slide 84
Pitch
Roll
Yaw
iFBalance
Roll, Pitch, Yaw (rpy)

## Slide 85
Front
Back
Pitch + Offset
Setpoint
0
Pitch
Roll
Yaw
iFBalance
Roll, Pitch, Yaw

## Slide 86
Quaternion
iFBalance
a + bi + cj + dk

## Slide 87
Rotation Matrix from Quaternion
iFBalance

## Slide 88
From Quaternion to Euler Angle
iFBalance
Roll
Pitch
Yaw

## Slide 89
iFBalance
Roll, Pitch, Yaw
(Flow Chart)
Quaternion Filter
(MAHONY / MADGWICK / No Filter)
Update Accelerometer
Update Gyroscope
Update Magnetometer
Rotation Matrix
Euler Angle

## Slide 90
iFBalance
10th Program
Accelerometer, Gyroscope, & Magnetometer data from MPU9250
Indifrog Blog (MPU 9250)

## Slide 91
iFBalance
7. Time of Flight (ToF) Sensor

## Slide 92
iFBalance
Field-of-View (FoV): 25 °
Time-of-Flight (ToF)
IR ranging sensor
2 Meter
I2C
Time of Flight (ToF)

## Slide 93
300+ mm Detection
FoV 25º
Multi Target Detection
VL53L3CX

## Slide 94
iFBalance
VL53L3CX

## Slide 95
Chip On/Off
VL53L3CX

## Slide 96
VL53L3CX

## Slide 97
iFBalance
12th Program
Measure Obstacle Distance Using
ToF Sensor
Indifrog Blog (ToF Sensor)

## Slide 98
VL53L3CX
./.pio/libdeps/pico32/STM32duino/VL53L3CX/src/vl53lx_class.h
// VL53LX(TwoWire *i2c, int pin) : RangeSensor(), dev_i2c(i2c), gpio0(pin)
// {
// Dev = &MyDevice;
// memset((void *)Dev, 0x0, sizeof(VL53LX_Dev_t));
// MyDevice.I2cHandle = i2c;
// MyDevice.I2cDevAddr = VL53LX_DEFAULT_DEVICE_ADDRESS ;
// }
VL53LX() : RangeSensor()
{
dev_i2c = &Wire;
gpio0 = -1;
Dev = &MyDevice;
memset((void *)Dev, 0x0, sizeof(VL53LX_Dev_t));
MyDevice.I2cHandle = dev_i2c;
MyDevice.I2cDevAddr = VL53LX_DEFAULT_DEVICE_ADDRESS ;
}

## Slide 99
VL53L3CX
./.pio/libdeps/pico32/STM32duino/VL53L3CX/src/vl53lx_class.h
VL53LX_Error InitSensor(uint8_t address)
{
VL53LX_Error status = VL53LX_ERROR_NONE;
//comment
// VL53LX_Off();
// VL53LX_On();
VL53LX_software_reset();
status = VL53LX_SetDeviceAddress(address);
…………………………..

## Slide 100
iFBalance
Special Program
Conflict between two I2C Device
Indifrog Blog (I2C Devices Conflict)

## Slide 101
iFBalance
8. Proportional Integral Derivative (PID)

## Slide 102
iFBalance
Proportional
Integration
Differentiation
PID Control

## Slide 103
Closed Loop Control
iFBalance
- The current output status is reflected in the control
control by reflecting the difference between the set point () and the robot pitch ()
Opened Loop Control
Controller
Process
- It does not reflect the current output status
r(t)
u(t)
y(t)
Process
Controller
Sensor
r(t)
u(t)
y(t)
e(t)
Error
Control signal
Output
Reference
Measured value

## Slide 104
iFBalance
Proportional
Integration
Differentiation
∝ error
steady state error
Overshoot Stability
PID Control

## Slide 105
iFBalance
GIF credit: https://commons.wikimedia.org/wiki/File:PID_Compensation_Animated.gif
PID Control

## Slide 106
iFBalance
Set
Set 𝑘_𝑝
Set & = 0
Set 𝑘_𝑖 & 𝑘_𝑑 = 0
Set
Set 𝑘_𝑖
Fixed
Fixed 𝑘_𝑝
Set
Set 𝑘_𝑑
Fixed & Fixed
Fixed 𝑘_𝑝 & Fixed 𝑘_𝑖
Start from (–) pitch value
Stop at (+) pitch value
Increase
Increase 𝑘_𝑝
is set0
𝑘_𝑝 is set0
Increase
Increase 𝑘_𝑖
Pitch repeats between (+) & (-)
Stop at uniform vibration
Stop 𝑘_𝑖 at uniform vibration
Stop at minimum overshoot
PID Control

## Slide 107
iFBalance
P
I
D
e(t)
Setpoint
Pitch
Process
Proportional
Integral
Differential
IMU Sensor
PWM Motor Control
y(t)
u(t)
r(t)
PID Controller
Measured value
Reference

## Slide 108
PID Control
iFBalance
Proportional
Integral
Differential
P
I
D
Error
Setpoint
Output
Pitch
Front
Back
Pitch + Offset
Setpoint
0
Output
Measurement
IMU Sensor
PWM Motor Control
Time Interval ( Unit : Second ) : 0.005 sec
Input
System
System Variable

## Slide 109
iFBalance
System
PID
Setpoint
Output
Pitch
Measurement
Input
Mixer
Left
Right

## Slide 110
iFBalance
PID
Setpoint
Output
Pitch
Measurement
Input
System
PID
Setpoint
Output
Pitch
Measurement
Input

## Slide 111
iFBalance
Ziegler–Nichols method
 Heuristic PID control method
https://en.wikipedia.org/wiki/Ziegler%E2%80%93Nichols_method
PID Control

## Slide 112
iFBalance
PID Control
Level PID
Pitch Value from IMU
Rate PID
Pitch Value
+
Gyrosensor value
from IMU

## Slide 113
iFBalance
11th Program
Speed control with PID
Indifrog Blog (PID)

## Slide 114
9. IR Sensor Module

## Slide 115
ADC1 Channels GPIO
Channel 0 IO36
Channel 1 IO37
Channel 2 IO38
Channel 3 IO39
Channel 4 IO32
Channel 5 IO33
Channel 6 IO34
Channel 7 IO35
ESP32 ADC (Group 1)

## Slide 116
Left Most
Left Back
Left Front
Right Most
Right Font
Right Back
Center
IR Sensor Position

## Slide 117
IR Sensor Pair  GPIO
Sensor Location GPIO
Left Most (LL) GPIO5
Center (CC) GPIO5
Right Most (RR) GPIO5
Left Back GPIO4
Right Front GPIO4
Left Front GPIO20
Right Back GPIO20
Group 1
Group 2
Group 3

## Slide 118
iFBalance
13th Program
Read IR Sensor Module
Indifrog Blog (IR Sensor)

## Slide 119
https://blog.naver.com/serimo/222007740015
1cm
iFBalance
Line Track Specification and IR Sensor Placement

## Slide 120
iFBalance
Find Indifrog at Naver Blog
Find Indifrog at Instagram
Find Indifrog at Youtube
Find INDIFROG at Facebook
Our Website https://www.indifrog.co.kr/